## Slide 1
1
Lecture:
IMAGE PROCESSING
Chapter 4:
Image Filtering
HCMC University of Technology and Education
Faculty of Electrical & Electronic Engineering
Assoc. Prof. Nguyen Thanh Hai
Notes: 1

## Slide 2
Image Filtering
INTRODUCTION
* Filtering in the spatial domain
Linear filtering is a weighted mask used to express the effects of the filter on each pixel of the image.
* Filtering in the frequency domain
Lots of noises: Gauss, impulse, etc.
Filters: lowpass, highpass, bandpass.
Image Filtering allows to apply various effects on images in order to filter noise or to smooth image.
The 2D filter is a 2D filter matrix

## Slide 3
Image Filtering
IMAGE FILTERING IN THE SPATIAL DOMAIN
A spatial filter means that a typical pixel in image is calculated based on neighborhood pixels. The filter is moved to all image pixels to create the output image.
Fig 4.1 describes a 3x3 spatial filter. Assume that one needs to calculate an image pixel in an image, the corresponding pixel of the output image is calculated by the sum of products of coefficients (values) between the filter and the image.

## Slide 4
Image Filtering
- Some applications in frequency domain, one often uses the FT.
Image filtering in the frequency domain
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 5
Image Filtering
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 6
Image Filtering
According to diagram of Fig above, frequency filtering can be expressed in MATLAB using the following functions:
function g=dftfilt(f,H)
F=fft2(f,size(H,1),size(H,2));
G=H.*F;
g=ifft2(G);
f=real(g);
g=g(1:size(f,1),1:size(f,2))
end
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 7
Image Filtering
Ex 4.7: Express image filtering in the spatial domain using Sobel and in the frequency domain using DFT
clear all;
f=imread('cameraman.tif');
h=fspecial('sobel');
sizeH=size(f)*2;
H=freqz2(h,sizeH);
H1=ifftshift(H);
gd=dftfilt(f,H1);
gs=imfilter(double(f),h);
d=abs(gd-gs);
gd=uint8(gd);imshow(gd);
gd=uint8(gd);imshow(gs);
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 8
Image Filtering
Checking homologous between two methods:
In which gs is the image filtered in the spatial and gd is filtered in the frequency, results as in Fig. 4.6
Fig. 4.7. Sobel filter
(a). in the frequency
(b) in the spatial
(c) differential
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 9
Image Filtering
Lowpass Filter: blurring image
* Ideal LowPass Filter - ILPF) : the transfer function is described as:
where is the cut-off frequency with non-negative value, is the distance from to the filter center. Orbit of is a circle.
* Butterworth LowPass Filter - BLPF) with n orders, the cut-off frequency , the transfer function is described as:
Often define the cut-off frequency at positions of (reduce 50% compared with the max value 1) when .
Calculate an example

## Slide 10
Image Filtering
Lowpass Filter: blurring image
* Ideal LowPass Filter - ILPF) : the transfer functions is described as:
where is the cut-off frequency with non-negative value, is the distance from to the filter center. Orbit of is a circle.
For example:
The original image f and the Fourier coefficient image.

## Slide 11
Image Filtering
Lowpass Filter: blurring image
The centered Fourier image.
Convert the center of image (u-H/2, v-W/2), in this case H=W=4, (u-2, v-2).
The centered image.
The pixel positions of the original image.

## Slide 12
Image Filtering
Lowpass Filter: blurring image
The filtered image.
Sqrt(u2+v2)<=D0; Assume that D0=H/2=4/2=2

## Slide 13
Image Filtering
Lowpass Filter: blurring image
The image after filtering
g =
0.25 + 0.1250i -0.125 - 0.25i 0.1250i -0.125
-0.125 - 0.25i 0.75 + 0.375i -0.625 -0.1250i
0.125i -0.625 0.75 - 0.375i -0.125 + 0.25i
-0.125 -0.1250i -0.125 + 0.25i 0.25 - 0.125i
g_non-negative integer =
0 0 0 0
0 1 0 0
0 0 1 0
0 0 0 0
g_real =
0.25 -0.125 0 -0.125
-0.125 0.75 -0.625 0
0 -0.625 0.75 -0.125
-0.125 0 -0.125 0.25
>=0.5 ; 1 and <0.5; 0

## Slide 14
Image Filtering
Transfer function of the Gaussian Lowpass Filter (GLPF) is expressed as follows:
In which is the standard deviation. If , we have :
When , the value at the cut-off frequency is . Fig. 4.7 describes the 3-D shapes of the frequency response of every filter.
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 15
Image Filtering
Fig. 4.7. left column: 3-D shape of the window filter; middle columns: images of the filters; right one: the frequency response of the ideal filters. First row: the ideal lowpass filter; middle one: the Butterworth lowpass filter; last one: the Gaussian lowpass filter

## Slide 16
Image Filtering
EX: Build a lowpass filter function as lpfilter with 3 basic filters.
function [H,D]=lpfilter(type,M,N,DO,n)
[U,V]=dftuv(M,N);
D=sqrt(U.^2+V.^2);
switch type
case 'ideal'
H=double(D<=DO);
case 'btw'
if nargin==4
n=1;
end
H=1./(1+(D./DO).^(2*n));
case 'gaussian'
H=exp(-(D.^2)./(2*(DO^2)));
otherwise
error('Unknown filter type');
end
Some functions in toolbox:
- mesh(H): express information in 3D such as x=1:M và y=1:N, with [M,N]=size(H).
- mesh(H(1:k:end,1:k:end))
- colormap([0 0 0]): black-white

## Slide 17
Image Filtering
Ex 4.3: express the plot using mesh for the Butterworth lowpass filter with different orders.
clear all;
BLPF1=fftshift(lpfilter('btw',500,500,50,1));
mesh(BLPF1(1:10:500,1:10:500));
axis([0 50 0 50 0 1]);
saveas(gcf, 'Hinh3.7a.tif', 'tif');
BLPF2=fftshift(lpfilter('btw',500,500,50,2));
figure;mesh(BLPF2(1:10:500,1:10:500));
axis([0 50 0 50 0 1]);
saveas(gcf, 'Hinh3.7b.tif', 'tif');
BLPF3=fftshift(lpfilter('btw',500,500,50,3));
figure;mesh(BLPF3(1:10:500,1:10:500));
axis([0 50 0 50 0 1]);
saveas(gcf, 'Hinh3.7c.tif', 'tif');
BLPF4=fftshift(lpfilter('btw',500,500,50,4));
figure;mesh(BLPF4(1:10:500,1:10:500));
axis([0 50 0 50 0 1]);
saveas(gcf, 'Hinh3.7d.tif', 'tif');
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 18
Image Filtering
BLPF3=fftshift(lpfilter('btw',500,500,50,3));
figure;mesh(BLPF3(1:10:500,1:10:500));
axis([0 50 0 50 0 1]);
saveas(gcf, 'Hinh3.7c.tif', 'tif');
BLPF4=fftshift(lpfilter('btw',500,500,50,4));
figure;mesh(BLPF4(1:10:500,1:10:500));
axis([0 50 0 50 0 1]);
saveas(gcf, 'Hinh3.7d.tif', 'tif');
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 19
Image Filtering
Fig 4.8. Plots of the Butterworth lowpass filters with different orders.
(a) Order 1
(b) Order 2
(c) Order 3
(d) Order 4
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 20
Image Filtering
Ex 4.4: express the lowpass filter with different cut-off frequencies and compare results
clear all;
f=imread('cameraman.bmp');
D01=1/5*size(f,1);
[M,N]=size(f);
[H,D]=lpfilter('ideal',2*M,2*N,D01);
g=dftfilt(f,H);
D02=2/5*size(f,1);
[M,N]=size(f);
[H,D]=lpfilter('ideal',2*M,2*N,D02);
g=dftfilt(f,H);
D03=3/5*size(f,1);
[M,N]=size(f);
[H,D]=lpfilter('ideal',2*M,2*N,D03);
g=dftfilt(f,H);
D04=4/5*size(f,1);
[M,N]=size(f);
[H,D]=lpfilter('ideal',2*M,2*N,D04);
g=dftfilt(f,H);
D05=size(f,1);
[M,N]=size(f);
[H,D]=lpfilter('ideal',2*M,2*N,D04);
g=dftfilt(f,H);
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 21
Image Filtering
Fig 4.9. cameraman image after the ideal lowpass filter with different cut-off frequencies
(a) Original image
(b)
(c)
(d)
(e)
(f)

## Slide 22
Image Filtering
Ideal highpass filter
If the transfer of the lowpass filter is , we have the highpass filter as follows:
Build the highpass filter function using Matlab
function H=hpfilter(type,M,N,D0,n)
if nargin==4
n=1;
End
Hlp=lpfilter(type,M,N,D0,n);
H=1-Hlp;
end
The ideal highpass filter is often implemented to filter image sharper by eliminating the low frequencies

## Slide 23
Image Filtering
Ex 4.5: Express the highpass filter using the function mesh for image.
clear all;close all;clc
ILPF=fftshift(hpfilter('ideal',500,500,50));
mesh(ILPF(1:10:500,1:10:500));
axis([0 50 0 50 0 1]);
BLPF=fftshift(hpfilter('btw',500,500,50));
mesh(BLPF(1:10:500,1:10:500));
axis([0 50 0 50 0 1]);
GLPF=fftshift(hpfilter('gaussian',500,500,50));
mesh(GLPF(1:10:500,1:10:500));
axis([0 50 0 50 0 1]);
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 24
Image Filtering
(a)
(b)
(c)
(d)
(e)
(f)
Fig. 4.10. Express the highpass filter. Top row: mesh with the 3-D shape; bottom row: 2D images of the mesh; left column: the ideal highpass filter, middle columns: the Butterworth highpass filter, right one: the Gaussian highpass filter
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 25
Image Filtering
The highpass filter is normalized to be zero to the DC components. Thus, this will reduce the average value of the image onto zero.
For improvement, the DC offset components are added to the highpass filter.
The high frequency emphasis filtering with offset is expressed as follows:
In which is the offset, denotes the multiplication constant and describes the transfer of the highpass filter.
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 26
Image Filtering
Ex 4.6: express the high frequency emphasis filtering using Matlab.
clear all;
f=imread('satellite.tiff');
[M N]=size(f);
D0=0.1*size(f,1);
HBW=hpfilter('btw',2*M,2*N,D0);
H=0.5+2*HBW;
gbw=dftfilt(f,HBW);
gbw=gscale(gbw);
ghf=dftfilt(f,H);
ghf=gscale(ghf);
ghe=histeq(ghf,256);
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 27
Image Filtering
In the Ex 4.6, the gscale allows to normalize and change data type containing the gray intensity in image. The gscale function is proposed:
function g=gscale(f)
fmin=min(f(:));
fmax=max(f(:));
for i=1:size(f,1)
for j=1:size(f,2)
g(i,j)=255*(f(i,j)-fmin)/(fmax-fmin);
end
end
g=uint8(g);
end
IMAGE FILTERING IN THE FREQUENCY DOMAIN

## Slide 28
Image Filtering
Ex 4.11. Satellite image after the highpass filter
(a) Blurring satellite image
(b) Image after the Butterworth highpass filter
(c) Image after the emphasis highpass filter
(d) Image after the histogram equalization of image (c)

## Slide 29
29
Assoc. Prof. Nguyen Thanh Hai
Image Filtering
Problem: Calculate the convolution of the image A and the mask h.
Suppose the input image is
And the kernel (mask)
HCMC University of Technology and Education
Faculty of Electrical & Electronics Engineering
Notes: 29

## Slide 30
30
  The End
Image Filtering
HCMC University of Technology and Education
Faculty of Electrical & Electronics Engineering
Assoc. Prof. Nguyen Thanh Hai
Notes: 30