## Slide 1
1
Lecture:
IMAGE PROCESSING
Chapter 3:
Fourier Transforms
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Nguyen Thanh Hai, PhD
Notes: 1

## Slide 2
2
Nguyen Thanh Hai, PhD.
Image Transform
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Fourier transform
What is Fourier transform?
What is obtained when using the Fourier transform?
Show an example with a 3x3 matrix and apply this Fourier transform.
Show formula of the Fourier transform.
What is Inverse Fourier transform?
Notes: 2

## Slide 3
3
Nguyen Thanh Hai, PhD.
Fourier Transform
Introduction
- Fourier Transform (FT): an image in the spatial is transformed to consider in the frequency domain. One can use the FT in filtering image or others
FT of two-dimensional (2D)
Properties of Discrete Fourier Transform
Applications
Extracting feature of image based on frequency
Filtering noise
Determining frequencies in an image
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 3

## Slide 4
4
Nguyen Thanh Hai, PhD.
Fourier Transform
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Brief Description
Frequency filters process an image in the frequency domain.
The image is Fourier transformed, multiplied with the filter
function and then re-transformed into the spatial domain.
Attenuating high frequencies results in a smoother image
in the spatial domain, attenuating low frequencies enhances the edges.
All frequency filters can also be implemented in the spatial
domain and, if there exists a simple kernel for the desired
filter effect, it is computationally less expensive to perform
the filtering in the spatial domain. Frequency filtering is more
appropriate if no straightforward kernel can be found in the
spatial domain, and may also be more efficient.
Notes: 4

## Slide 5
5
Nguyen Thanh Hai, PhD.
Fourier Transform
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 5

## Slide 6
6
Nguyen Thanh Hai, PhD.
Fourier Transform
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 6

## Slide 7
7
Nguyen Thanh Hai, PhD.
Fourier Transform
Top row: a signal and its Fourier transform. Middle row: the unit sample response function of a filter on the left, and the filter's system
function on the right
University of Technology and Education
Faculty of Electrical & Electronic Engineering
1D Fourier Transform
Notes: 7

## Slide 8
8
Nguyen Thanh Hai, PhD.
Fourier Transform
Bottom row: On the left the filtered signal that can be obtained by convolving the signal at the top with the filter in the middle. On the right the Fourier transform of the filtered signal obtained by multiplying the Fourier transform of the signal at the top, with the Fourier transform (system function) of the filter in the middle
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 8

## Slide 9
Nguyen Thanh Hai, PhD
Image Transforms
University of Technology and Education
Faculty of Electrical & Electronic Engineering
One-Dimensional Discrete Fourier Transform
The Fourier transform of a discrete function of one variable, f(x), x=0,1,2,…,M-1, is given by the equation
; For u=0,1,2,…M-1
Similarly, its the inverse Fourier transform is determined as follows:
; For x=0,1,2,…M-1
The 1/M multiplier in front of the Fourier Transform sometimes is placed in front of the inverse instead. Sometimes, both equations are multiplied by 1/

## Slide 10
Nguyen Thanh Hai, PhD
Image Transforms
University of Technology and Education
Faculty of Electrical & Electronic Engineering
One-Dimensional Discrete Fourier Transform
The concept of the frequency domain, mentioned numerous times follows from Euler’s formula:
We have , it gives us
The values of f(x) are multiplied by cosines and sines of various frequencies, so the values of F(u) are expressed in the frequency domain

## Slide 11
Nguyen Thanh Hai, PhD
Image Transforms
Example : Consider the time signal shown in Fig. 2.1. The DFT of this signal is shown in Fig. 2.2.
Fig. 2.1: Signal x, defined in the time domain
Fig. 2.2: Magnitude of the DFT of signal x
University of Technology and Education
Faculty of Electrical & Electronic Engineering

## Slide 12
12
Nguyen Thanh Hai, PhD
Image Transforms
Two-Dimensional Discrete Fourier Transform
The 2D FT is a rather straightforward extension of the 1D transform. Mathematically, the 2D DFT is defined as:
where u=0,1,…,M-1 and v=0,1,…,N-1 are the frequency axes, in which G(u,v) is described as a Fourier image.
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 12

## Slide 13
13
Nguyen Thanh Hai, PhD
Image Transforms
Two-Dimensional Discrete Fourier Transform
The inverse transformation, the 2D IDFT is denoted as:
where x=0,1,…,M-1 and y=0,1,…,N-1 and g(x,y) is an image after inverse transform.
University of Technology and Education
Faculty of Electrical & Electronic Engineering
The variables u and v are the transform or frequency variables, and x and y are the spatial or image variables. Sometime 1/MN is found in front of the inverse. Other times, the multiplier is located in front of both the Fourier Transform and the inverse.
Notes: 13

## Slide 14
14
Nguyen Thanh Hai, PhD
Image Transforms
The kernel of DFT is a complex function  these images are complex:
  Real parts
  Imaginary parts
Display the DFT of an image
  Coefficients of the high frequency are small.
  Logarithmic function
University of Technology and Education
Faculty of Electrical & Electronic Engineering
The Fourier spectrum, phase angle, and power spectrum of 2D transform are expressed as follows:
where R(u,v) and I(u,v) are the real and imaginary parts of F(u,v), respectively.
Notes: 14

## Slide 15
15
Nguyen Thanh Hai, PhD
Image Transforms
Solution:
- One has the row, M=4 ; the column, N=4
- Transform matrix U(x,u) using the formula:
Using the formula of Euler, we have
Example: Find the Fourier transform of the following 4x4 image
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 15

## Slide 16
16
Nguyen Thanh Hai, PhD
Image Transforms
Two-Dimensional Discrete Fourier Transform
The 2D FT is a rather straightforward extension of the 1D transform. Mathematically, the 2D DFT is defined as:
where u=0,1,…,M-1 and v=0,1,…,N-1 are the frequency axes, in which G(u,v) is described as a Fourier image.
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Calculate directly an image using this function
Notes: 16

## Slide 17
17
Nguyen Thanh Hai, PhD
Image Transforms
University of Technology and Education
Faculty of Electrical & Electronic Engineering
g
Biến đổi Fourier của với việc tính toán từng giá trị cụ thể tại từng vị trí, chẳng hạn như với và .
G
Notes: 17

## Slide 18
18
Nguyen Thanh Hai, PhD
Image Transforms
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Ví dụ 3.1: Biến đổi Fourier không dùng hàm có sẵn trong MATLAB
clear all;clc
a=zeros(4,4);
a(2:3,2:3)=1;
%a =[0 0 0 0; 0 1 1 0; 0 1 1 0; 0 0 0 0]
[M,N]=size(a)
for u=1:M % size(a,1)
for v=1:N% size(a,2)
for x=1:size(a,1)
for y=1:size(a,2)
phi=(2*pi*(u-1)*(x-1)+2*pi*(v-1)*(y-1))/4;
p(x,y)=complex(cos(phi),-sin(phi));
end
end
F(u,v)=sum(sum(p.*a));
end
end
Notes: 18

## Slide 19
19
Nguyen Thanh Hai, PhD
Image Transforms
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Central shift
The value of the transform at (u,v)=(0,0) can be determined using the following equation:
In which because of two frequencies u=0 and v=0, their exponential functions are zero and F(0,0) is equal to the average gray level of the image, called the dc component of the spectrum (similar to current of zero frequency in electronic engineering)
In which u=0,1,2,…M-1, v=0,1,2,…M-1, u,v are integers
Notes: 19

## Slide 20
20
Nguyen Thanh Hai, PhD
Image Transforms
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Central shift
In order to guarantee that the shifted coordinates are integers, we require that M and N are even.
When implementing the FT in a computer, the limits of summations are from u=1 to M and v=1 to N. The actual center of the transform is u=(M/2)+1 and v=(N/2)+1
A value of c-0.5 can be used in the transformation in order to decrease overall intensity.
For having a look easy, most Fourier spectra are processed by a log transformation
in which M = N.
Notes: 20

## Slide 21
21
Nguyen Thanh Hai, PhD
Image Transforms
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 21

## Slide 22
Nguyen Thanh Hai, PhD
Image Filtering
Central shift
University of Technology and Education
Faculty of Electrical & Electronic Engineering
The centered Fourier image.
Convert the center of image
Fc(u,v)=(u-H/2, v-W/2)
in this case H=W=4, (u-2, v-2).
The centered image.
The pixel positions of the original image.

## Slide 23
Nguyen Thanh Hai, PhD
Image Filtering
Central shift
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Fourier image without central shift
Fourier image after central shift

## Slide 24
24
Nguyen Thanh Hai, PhD
Image Transforms
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Image of a 20 x 40 white rectangle on a black background of size 512 x 512 pixels.
Centered Fourier spectrum shown after application of the log transformation
Notes: 24

## Slide 25
25
Nguyen Thanh Hai, PhD
Image Transforms
F=fft2(f)
This function will return image of FT with the size, having data arranged as in Fig. and the axis origin will be the upper left side of image and the end period is at the frequency rectangular center.
(a) Fourier spectrum with size and four quad angles of the period; (b) Fourier spectrum with size with the center origin of frequency. This stectrum is obtain by multiplying the function and before using the FT.
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 25

## Slide 26
26
Nguyen Thanh Hai, PhD
Image Transforms
Some functions for Fourier transform:
F=fft2(f)
Amplitude spectrum of Fourier transform:
S=abs(F)
The center shift, Fc=fftshift(F)
Fig. (a). Original image; (b) Fourier spectrum with the center at the foue quad angles; (c) Fourier spectrum shifted with the center at the coordinate origin; (d) Fourier spectrum represented using log transform
University of Technology and Education
Faculty of Electrical & Electronic Engineering
CMR:
Notes: 26

## Slide 27
27
Nguyen Thanh Hai, PhD
Image Transforms
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Fourier transform of g(x,y) with the center shift, calculating each pixel value in output image at coordinate, for example, calculate G(u,v), with .
Example
Re-calculating
Notes: 27

## Slide 28
28
Nguyen Thanh Hai, PhD
Image Transforms
University of Technology and Education
Faculty of Electrical & Electronic Engineering
0 0 0 0
0 - 2j -2 + 2j 2
0 -2 + 2j 4 2 – 2j
0 2 -2 – 2j 2j
Notes: 28

## Slide 29
29
Nguyen Thanh Hai, PhD
Image Transforms
Ví dụ 3.2: Perform the FT of image and calculate its Fourier spectrum.
clear all;
close all;
f=imread('TestDFT.tif');
F=fft2(f);
S=abs(F);
Fc=fftshift(F);
Sc=abs(Fc);
S2=log(1+abs(Fc));
figure;
subplot(2,2,1);imshow(f);
subplot(2,2,2);imshow(S);
subplot(2,2,3);imshow(Sc);
subplot(2,2,4);imshow(S2);
Functions: “fftshift” and “ifftshift” will transfer the angle position into the original one.
F=ifftshift(Fc)
The inverse FT
f=ifft2(F)
F is the FT, f is image in the spatial domain. If the input of F is real, f is real. However, in practice, function ifft2 often has a small complex value, its result will be complex, so we can use function to produce real values:
f=real(ifft2(F))
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 29

## Slide 30
30
Nguyen Thanh Hai, PhD
Image Transforms
(a) Fourier spectrum (fft) with size and 4 angles of rectangle. (b) Spectrum is calculated by product of and before calculating the FT.
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 30

## Slide 31
31
Nguyen Thanh Hai, PhD
Image Transforms
Amplitude of the Fourier spectrum using function S=abs(F)
(a). Original image; (b) Fourier spectrum; (c) Fourier spectrum with shifted center; (d) Enhanced spectrum using the log transformation
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 31

## Slide 32
32
Nguyen Thanh Hai, PhD
Image Transforms
Exercise
Compute the DFT of the following image
Solution
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 32

## Slide 33
33
Nguyen Thanh Hai, PhD
Image Transforms
Exercise
Verify the relationship of the DFTs of the following images
A
B
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 33

## Slide 34
34
Image Transforms
Exercise
Find the DFT of the following image
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 34

## Slide 35
35
Image Transforms
Exercise
Solution
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 35

## Slide 36
36
Nguyen Thanh Hai, PhD
Image Transforms
Creat the function fft2_new.m to calculate Fourier transform of an image
function G=fft2_new(g)
% G is fourier tranform of g
%===================
% Get size of matrix f
M=size(g,1); % get number of rows
N=size(g,2) ; % get number of columns
%===================
%create matrix U
%U(x,u)=exp(-j*2*pi*x*u/M)
% x, u run from 0 to M-1
U=[ ];
for x=0:M-1
for u=0:M-1
U(x+1,u+1)=exp(-j*2*pi*m*p/M);
end
end
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 36

## Slide 37
37
Nguyen Thanh Hai, PhD
Image Transforms
Creat the function fft2_new.m to calculate Fourier transform of an image
%===================
% create matrix V
%V(y,v)=exp(-j*2*pi*y*v/N)
% y, v run from 0 to N-1
V=[ ];
for y=0:N-1
for v=0:N-1
V(y+1,v+1)=exp(-j*2*pi*y*v/N);
end
end
%===================
%Fourier transform
G=U*g*V;
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 37

## Slide 38
38
Nguyen Thanh Hai, PhD
Image Transforms
function g=ifft2_new(G)
% g is invert fourier tranform of G
%===================
%Get size of matrix G
M=size(G,1); % get number of rows
N=size(G,2) ; % get number of columns
%===================
Creat the inverse function ifft2_new.m to calculate inverse Fourier transform of an image
%===================
%create matrix U
%U(m,p)=exp(-j*2*pi*x*u/M)
% x, u run from 0 to M-1
U=[ ];
for x=0:M-1
for u=0:M-1
U(x+1,u+1)=exp(-j*2*pi*x*u/M);
end
end
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 38

## Slide 39
39
Nguyen Thanh Hai, PhD
Image Transforms
Test and compare two results on Matlab fft2 and ifft2
% Test and compare together G1 and G2, g1 và g2
g=[0 0 0 0; 0 1 1 0; 0 1 1 0; 0 0 0 0]
G1=fft2(g)
G2=fft2_new(g)
g1=ifft2(G1)
g2=ifft2_new(G1)
MAGNITUDE(G) = SQRT( REAL(G)^2+IMAGINARY(G)^2 )
PHASE(F) = ATAN( IMAGINARY(G)/REAL(G) )
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Notes: 39

## Slide 40
Nguyen Thanh Hai, PhD
Image Transforms
Example 3.6: Consider the image g(x,y) shown in Fig. 3.3. Calculate the 2D DFT of this image.
Fig. 3.3: Image in the time domain
Fig. 3.4: Magnitude of the DFT of image
University of Technology and Education
Faculty of Electrical & Electronic Engineering

## Slide 41
Nguyen Thanh Hai, PhD
Image Transforms
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Example:
Fig. 3.5: Image and Magnitude of the DFT of image in 3D display

## Slide 42
Nguyen Thanh Hai, PhD
Image Transforms
University of Technology and Education
Faculty of Electrical & Electronic Engineering
Example: tính toán và viết code matlab
Ảnh là ma trận 4x4 với 4 số 1 ở giữa và tất cả pixel còn lại là zero
Xác định ảnh Fourier
Xác định ảnh biên độ phổ của ảnh Fourier
Xác định ảnh dịch tâm
Xác định ảnh Log
Tính góc pha của ảnh Fourier
Tính ảnh phổ công suất
Xác định ảnh biến đổi Fouier ngược
Dịch tâm ngược
Tự viết lại hàm biến đổi Fourier
f = ones(30,30);
f(5:24,13:17) = 0;

## Slide 43
Nguyen Thanh Hai, PhD
  The End
Image Transforms
University of Technology and Education
Faculty of Electrical & Electronic Engineering